## Slide 1
Design and Verification of AHB2APB Bridge using UVM
ECE593 – Fundamentals of Pre-Silicon Validation
  Team Members
  Daniel Jacobsen
  Balaji Ginkal Harisha
  Mohith Kumar Bennahatti Chikkegowda
  Akshaya Kudumalakunte Ravi Kumar

## Slide 2: Table of Contents:
Introduction
AHB2APB Bridge Overview
AHB Bus Protocol
APB Bus Protocol
AHB2APB Bridge
AHB2APB Bridge Functionality
Read and Write Transfer
Verification Plan
UVM Testbench Architecture
Test Cases
Simulation Results
Coverage report
Conclusion
References

## Slide 3: AHB2APB Bridge Overview
Purpose:
  Acts as an interface between AHB (Advanced High-Performance Bus) and APB (Advanced Peripheral Bus).
  Converts AHB transactions to APB transactions.
Key Features:
  Handles synchronization, protocol adaptation, and control signals.
  Supports pipelined AHB and non-pipelined APB protocols.

## Slide 4: AHB Bus Protocol
Features:
  High-performance, pipelined bus.
  Supports burst transfers, split transactions, and single-cycle handover.
Key Signals:
  HCLK(Bus clock)
  HRESETn
  HADDR[31:0]
  HWRITE[1:0]
  HBURST[2:0]
  HWDATA[31:0]
  HRDATA[31:0]
  HREADY
  HRESP

## Slide 5: APB Bus Protocol
Features:
  Low-power, simple bus for peripherals.
  Supports single-cycle read/write transactions.
Key Signals:
  PCLK
  PRESETn
  PENABLE
  PWRITE
  PADDR
  PWDATA
  PRDATA
  PREADY

## Slide 6: AHB2APB Bridge

## Slide 7: AHB2APB Bridge Functionality
Key Functions:
  Latches and decodes AHB addresses.
  Generates PSEL signals for APB peripherals.
  Converts AHB transactions to APB transactions.
  Handles wait states for synchronization.
Write Transfer:
  Converts HRDATA to PWDATA.
Read Transfer:
  Converts PRDATA to HRDATA.

## Slide 8: Read and Write Transfer

## Slide 9: Verification Plan
Verification Objectives:
  Ensure correct data transfer between AHB and APB.
  Verify protocol compliance (AHB and APB).
  Handle error conditions, and corner cases.
Verification Levels:
  Top-level module verification for end-to-end functionality.

## Slide 10: UVM Testbench Architecture
UVM Components:
  AHB Agent: Driver, Sequencer, Monitor.
  APB Agent: Driver, Sequencer, Monitor.
  Scoreboard: Compares expected vs. actual transactions.
Verification Flow:
  Build → Connect → Run → Check → Report.

## Slide 11: Test Cases
Test Types:
  Single Read/Write: Basic read/write operations.
  Burst Read/Write: Burst mode transactions.
  Corner Cases: Address boundary testing, error injection.

## Slide 12: Simulation Results
Single Read/Write: Basic read/write operations.

## Slide 13: Simulation Results
  Burst Read/Write: Burst mode transactions.

## Slide 14: Simulation Results
Corner Cases: Address boundary testing, error injection.
Address Mismatch
Dropped Transaction
Write Corruption

## Slide 15: Simulation Results
Combined Cases: Combined read/write and burst read/write.

## Slide 16: Coverage report:

## Slide 17: Conclusion
  Successfully designed and verified the AHB2APB bridge.
  Achieved high functional and code coverage.

## Slide 18: References
GitHub Repositories:
  AHB-to-APB-Bridge
  Pre_Silicon-AHB-to_APB-Verification
Tools:
  QuestaSim, EDA Playground.